## Slide 1: SYNTHESIS AND SIMULATION OF CORTEX M0 ARM Processor
K.SIVARANJINI
AYUSHI GUPTA
G DHARMIK

## Slide 2: INTRODUCTION
IN THIS PROJECT,WE ARE IMPLEMENTING A CIRCUIT WHICH TOGGLES BETWEEN TWO INPUT NUMBERS AT A GIVEN FREQUENCY.
THE OUTPUT IS DISPLAYED USING 8 LEDS REPRESENTING 8 BITS.
FOR EXAMPLE:IF NUMBER IS 42 IT IS REPRESENTED AS 0100 0010(i.e 2nd and 7th leds are on)

## Slide 3: Components
Keil simulator
Xlinx vivado
Basys 3 Artix-7 FPGA board
Cadence

## Slide 4: Procedure
The keil simulator is to be run .At this step,we get code.hex file.
This code.hex file is used in the xlinx code as memory.
From vivado, bitstream file is generated.
This is dumped onto a fpga board and we observe the led output
Then the layout is done on cadence.

## Slide 5: Keil simulator
In the code,a memory array is created using dcd.
Then the function of toggling values at a given frequency is done.

## Slide 6: Xlinx code
This module contains
cortexm0ds_logic.v
CORTEXM0INTEGRATION.v
AHBDCD.v
AHBMUX.v
AHB2BRAM.v
AHB2LED.v
AHBLITE_SYS.v

## Slide 7: Cortex processor
Cortex_m0_ds:This is generating all the signals required for a processor.
Cortex_mo integration:This is integrating the required sets to make processor module

## Slide 8: AHB bus component
AHBDCD.v:It has the input as address and the program decodes the program and creates the selector bits and mux selector bits
AHBMUX.v:It takes mux selector bits in the program it finds master-slave combination.

## Slide 9: AHB2BRAM.v
This is the program where bus and ram are connected.bram is on-chip memory.
This is circuit we integrate code.hex

## Slide 10: AHB2LED.V
This is the circuit which connects bus and led perpiherals.

## Slide 11: AHBLITE.v
This is the the program which connects all the blocks

## Slide 12: Implementation

## Slide 13: Troubles faced
Xlinx ise wasn’t working

## Slide 14: Future thoughts
Incremental Display:
We thought of implementing a program which takes two inputs where first input<second input. At every clock cycle, we thought of incrementing the first number until it reaches the second number.